## Slide 1
Nitrogen
The Good the Bad
and the Ugly….
and how it relates to Nitrogen Sensitive Areas and the “new” Title 5
George Heufelder M.S., R.S.
Gheufelder@capecod.gov

## Slide 2
Outline
Nitrogen – what’s the big deal and why are we so concerned ?
What changed in the “new” 310:CMR 15.000 (Title 5)
What has occurred to help address the new challenges

## Slide 3
Nitrogen – what’s the big deal and why are we so concerned ?
In a nutshell ….
Wastewater disposal practices like septic systems break down complex nitrogen into smaller molecules that pose both public health and environmental threats.

## Slide 4
Good
Bad
Ugly
Blue Skies
Food
NO “1992 molecule of the year”**
DNA
Protein
NITROGEN
Nitrates in Drinking Water
Eutrophication of marine environments
Toxic algae blooms
Anoxic Zones
Impaired water uses
**Research has proven the crucial role the gas plays in such fundamental biological processes as regulation of blood pressure, functioning and malfunctioning of the immune system, and activation of mechanisms in the central nervous system affecting everything from gastric motility to memory to behavior. https://www.ahajournals.org/doi/10.1161/01.cir.98.22.2365#:~:text=Nitric%20oxide%20was%20named%20%E2%80%9CMolecule,1998%2C%20in%20Stockholm%2C%20Sweden.
Methemoglobinemia
Cancer risks

## Slide 5
Thinking globally about reactive nitrogen
2.2 x 10 11 lbs
N2
8.8 x 10 10 lbs
4.4 x 10 10 lbs
6.6 x 10 10 lbs
6.6 x 10 9 -
2.2 x 10 10 lbs
Haber-Bosch
2.6 x 10 8 lbs
Fertilizer
Lightning
Crop management
Burning – marsh clearing etc.
NOx
Environmental Health Perspectives
Volume 112(10), 2004
?

## Slide 6
Nitrogen Cycle
The Big Picture
WE are part of the nitrogen cycle. We take in nitrogenous nutrients that ultimately came from organisms that fixed atmospheric nitrogen gas (or plants that got their nitrogen from commercial fertilizers). We excrete what nitrogen we don’t need, primarily as urea, into our septic tanks. Bacteria in the septic tank anaerobically ammonify the nitrogen. Other bacteria aerobically nitrify the ammonia in the soil as wastes pass through the leachfield. If we introduce nitrified waste to the right anoxic setting, we can denitrify the wastewater or turn the nitrate into nitrogen gas. And the cycle continues…..
The Zen of N

## Slide 7
For the most part
Microbes drive the train

## Slide 8
So, what’s new ?

## Slide 9
So, what’s new ?
It’s not just about drinking water resources anymore
Nitrogen
Sensitive
Areas

## Slide 10
Prequel Review
Title 5 - 1995
Title 5 - 2023
NSA
NSA
Focus on drinking water
Focus on drinking water
and additionally identified sensitive surface water receptors

## Slide 11
Review - NSAs prior to recent code changes
4 BEDROOMS PER ACRE
Why?
At 440 gallons per day, the total nitrogen (primarily nitrate) could meet an acceptable level of nitrogen in the groundwater (combined with other sources) as to not present a public health risk at the property line (5 mg/L?)
1995
Title 5 circa 1995 introduced the ability to increase the density to six bedrooms per acre using approved innovative/alternative septic systems that could meet a 19mg/L Total Nitrogen discharge limit
Drinking water protection

## Slide 12
Watershed - Any region or area measured in a horizontal topographic divide which directs water runoff from precipitation, normally by gravity, into a stream, a body of impounded surface water, or a coastal embayment, or any region or area measured by a groundwater divide which directs groundwater into a stream, a body of impounded surface water, or a coastal embayment.
The “new” NSAs
It’s all about watersheds
15.215: Designation of Nitrogen Sensitive Areas (emphasis added)

## Slide 13
Watersheds
are
analogous to
Zones of Contribution
(wellhead protection areas)
Both define the land areas that contribute/direct/influence groundwater or surface runoff toward a feature of concern.
Source: Cape Cod Commission - Water Resources Classification Map

## Slide 14
Coming soon to a theatre or watershed near you (if it’s not already there)
– the NEW Nitrogen Sensitive Areas -

## Slide 15
Groundwater divide
Sub watershed
MATTAPOISETT
ACUSHNET
FAIRHAVEN

## Slide 16
https://mass-eoeea.maps.arcgis.com/apps/webappviewer/index.html?id=96035fe034044e2596b49168b0e35d8e
MassDEP Designated Natural Resource Area Nitrogen Sensitive Areas
MassDEP has provided a lookup interactive map to determine whether a property in is a new NSA

## Slide 17
WATERSHEDS - THE NEW NITROGEN SENSITIVE AREAS
Nitrogen removal performance requirements need to be determined by the carrying capacity of the receiving waterbody (usually determined in process of compiling a watershed wastewater management plan).
Generally higher levels of performance and management will be required compared to drinking water NSAs

## Slide 18
Total
Maximum
Daily
Load
How much of a contaminant can you load on a contributing area without getting an undesired result at the point of interest ?
Or…

## Slide 19
Total Maximum Daily Load
How much of this ?
Before you get this
Or…

## Slide 20
Total Maximum Daily Load
How many of these ?
Before you get this

## Slide 21
Total Maximum Daily Load
Once you have these
How do you fix
this?

## Slide 22
ONE WAY
I/A Septic Systems
One of many ways to reduce
nitrogen loading

## Slide 23
How do Innovative/Alternative (I/A) septic systems reduce nitrogen loading?

## Slide 24
In a nutshell… Innovative Alternative Septic Systems (I/A) manipulate the nitrogen cycle in contained units to first oxidize reduced nitrogen (ammonium) to nitrate and then reducing nitrate to nitrogen gas.

## Slide 25
Types or broad classes of alternative onsite septic systems that remove nitrogen.
Trickling filters (various media)
Mixed liquor systems with some fixed film growth
Sequencing Batch Reactors
Membrane bioreactors
Woodchip Bioreactors
The mention or showing of any product does not represent and endorsement for its use by the Barnstable County Department of Health and the Environment

## Slide 26
Media Filters
with recirculation

## Slide 27
Mixed Liquor
and fixed film
some with recirculation
HOOT®

## Slide 28
Sequencing Batch Reactors

## Slide 29
Membrane
Bioreactors
some with recirculation

## Slide 30
Woodchip Bioreactors
https://www.lombardoassociates.com/nitrex.php

## Slide 31
The challenge of determining the true performance of Innovative/Alternative (I/A) septic systems

## Slide 32
Nitrogen Concentrations
Vs
Nitrogen Loads
Tale of two methods

## Slide 33
330 GPD
130 GPD
19 Lbs/Year
7.5 Lbs/Year
I/A System
I/A System
19 mg/L
19 mg/L
130 GPD
19 Lbs/Year
I/A System
48 mg/L
Bottom line – concentration is not the whole story but it’s the easiest measure of performance

## Slide 34
I/A System
I/A System
19 mg/L
What about varying INFLUENT numbers ?
Assume 130 gal/day usage two houses
Influent 90 mg/L
Influent 40 mg/L
System discharge 19mg/L
System discharge 19mg/L
Mass Load Reduction
79%
Mass Load Reduction
53 %

## Slide 35
Take Home Message
Without influent concentrations and water usage to determine the pre-treatment loads you can not calculate a true load reduction affected by any I/A system.

## Slide 36
Good
Better
Best
MassDEP provides information on the performance of Innovative/Alternative septic Systems and has established a list of Best Available Nitrogen Removal Technology
Data extracted from MassDEP website current 25-09-01

## Slide 37
https://www.mass.gov/info-details/approved-title-5-innovativealternative-technologies
GENERAL USE

## Slide 38
Data to support the classification as BANRT
Data extracted from MassDEP website current 25-09-01

## Slide 39
https://www.mass.gov/info-details/approved-title-5-innovativealternative-technologies
PROVISIONAL USE
Data extracted from MassDEP website current 25-09-01

## Slide 40
PROVISIONAL USE
NitROETM
NitrexTM
Data extracted from MassDEP website current 25-09-01

## Slide 42
Take Home
Nitrogen becomes a problem when our wastewater practices deposit reactive nitrogen where it intercepts drinking water wells or surface waters sensitive to reactive nitrogen inputs.
Title 5 included in its 2023 revisions a new class of Nitrogen Sensitive Areas (NSA), expanding the definition to include selected marine embayments (those designated by MassDEP based on established Total Maximum Daily Load Estimates).
Also included in the revised regulation is a definition of Best Available Nitrogen Reducing Technology and their application in certain areas.
MassDEP has established a series of web pages that help you lookup whether you are in a “new” NSA, and what septic system technologies can use in those areas.
Upgrade of septic systems in marine NSA is mandatory unless your town obtains a watershed permit.

## Slide 43
Questions?